## Slide 1: Computer Architecture and Operating Systems Lecture 9: Virtual Memory
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 3: Virtual Address Space
Virtual addresses
  Programs use virtual addresses
  Entire virtual address space stored on a hard drive
  Subset of virtual address data in DRAM
  CPU translates virtual addresses into physical addresses (DRAM addresses)
  Data not in DRAM fetched from hard drive
Memory Protection
  Each program has own virtual to physical mapping
  Two programs can use same virtual address for different data
  Programs don’t need to be aware others are running
  One program (or virus) can’t corrupt memory used by another

## Slide 4: Cache/Virtual Memory Analogues
Physical memory acts as cache for virtual memory
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number

## Slide 5: Virtual and Physical Addresses
Most accesses hit in physical memory
But programs have a large capacity of virtual memory

## Slide 6: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 7: Virtual Memory Example
System
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Organization
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)

## Slide 8: Virtual Memory Example
What is the physical address of virtual address 0x247C?
  VPN = 0x2
  VPN 0x2 maps to PPN 0x7FFF
  12-bit page offset: 0x47C
  Physical address = 0x7FFF47C

## Slide 9: Page Table
Used to perform address translation
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 10: Page Mapping

## Slide 11: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 12: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 13: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 14: Fast Translation Using a TLB

## Slide 15: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 16: TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not preset
Must recognize TLB miss before destination register overwritten
  Raise exception
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur

## Slide 17: TLB and Cache Interaction
If cache tag uses physical address
  Need to translate before cache lookup
Alternative: use virtual address tag
  Complications due to aliasing
    Different virtual addresses for shared physical address

## Slide 18: Memory Protection
Different tasks can share parts of their virtual address spaces
  But need to protect against errant access
  Requires OS assistance
Hardware support for OS protection
  Privileged supervisor mode (aka kernel mode)
  Privileged instructions
  Page tables and other state information only accessible in supervisor mode
  System call exception (e.g., ecall in RISC-V)

## Slide 19: Virtual Memory Summary
Virtual memory increases capacity
A subset of virtual pages in physical memory
Page table maps virtual pages to physical pages – address translation
TLB speeds up address translation
Different page tables for different programs provides memory protection

## Slide 20: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero