## Slide 1: Computer Architecture and Operating Systems Lecture 16: Data-level parallelism: Vector, SIMD, GPU
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Data-Level Parallelism
Data-level parallelism is parallelism achieved by performing the same operation on independent data
Best in dealing with arrays in for loops and processing other kinds of identically structured data
Unsuitable for control flow structures

## Slide 3: Instruction and Data Streams
An alternate classification
SPMD: Single Program Multiple Data
  A parallel program on a MIMD computer
  Conditional code for different processors
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345

## Slide 4: Types of Parallel Processing
Single instruction, single data (SISD) stream: A single processor executes a single instruction stream to operate on data stored in a single memory. Uniprocessors fall into this category.
Single instruction, multiple data (SIMD) stream: A single machine instruction controls the simultaneous execution of a number of processing elements on a lockstep basis. Each has an associated data memory, so that instructions are executed on different sets of data by different processors. Vector and array processors fall into this category.
Multiple instruction, single data (MISD) stream: A sequence of data is transmitted to a set of processors, each of which executes a different instruction sequence. Not commercially implemented.
Multiple instruction, multiple data (MIMD) stream: A set of processors simultaneously execute different instruction sequences on different data sets. SMPs, clusters, and NUMA systems fit into this category.

## Slide 5: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to RISC-V
  v0 to v31: 32 × 64-element registers, (64-bit elements)
  Vector instructions
    fld.v, fsd.v: load/store vector
    fadd.d.v: add vectors of double
    fadd.d.vs: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth

## Slide 6: Example: DAXPY (Y = a × X + Y)
Conventional RISC-V code:
fld f0,a(x3) # load scalar a
addi x5,x19,512 # end of array X
loop: fld f1,0(x19) # load x[i]
fmul.d f1,f1,f0 # a * x[i]
fld f2,0(x20) # load y[i]
fadd.d f2,f2,f1 # a * x[i] + y[i]
fsd f2,0(x20) # store y[i]
addi x19,x19,8 # increment index to x
addi x20,x20,8 # increment index to y
bltu x19,x5,loop # repeat if not done
Vector RISC-V code:
fld f0,a(x3) # load scalar a
fld.v v0,0(x19) # load vector x
fmul.d.vs v0,v0,f0 # vector-scalar multiply
fld.v v1,0(x20) # load vector y
fadd.d.v v1,v1,v0 # vector-vector add
fsd.v v1,0(x20) # store vector y

## Slide 7: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology

## Slide 8: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications

## Slide 9: Vector vs. Multimedia Extensions
Vector instructions have a variable vector width, multimedia extensions have a fixed width
Vector instructions support strided access, multimedia extensions do not
Vector units can be combination of pipelined and arrayed functional units:

## Slide 10: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 11: History of GPUs
Early video cards
  Frame buffer memory with address generation for video output
3D graphics processing
  Originally high-end computers (e.g., SGI)
  Moore’s Law  lower cost, higher density
  3D graphics cards for PCs and game consoles
Graphics Processing Units
  Processors oriented to 3D graphics tasks
  Vertex/pixel processing, shading, texture mapping, rasterization

## Slide 12: Example: NVIDIA Fermi
Multiple SIMD processors, each as shown:

## Slide 13: Example: NVIDIA Fermi
SIMD Processor: 16 SIMD lanes
SIMD instruction
  Operates on 32 element wide threads
  Dynamically scheduled on 16-wide processor over 2 cycles
32K x 32-bit registers spread across lanes
  64 registers per thread context

## Slide 14: GPU Memory Structures

## Slide 15: Concluding Remarks
SIMD and vector operations match multimedia applications and are easy to program

## Slide 16: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero