## Slide 1: Computer Architecture and Operating Systems Lecture 16: Domain-specific architectures. Tensor Processing Unit.
Alexey Kanakhin
akanakhin@hse.ru

## Slide 2: Conventional 5-stages pipeline

## Slide 3: Possible improvements
Modern performance tuning techniques:
  Deep memory hierarchy
  Wide SIMD units
  Deep pipelines
  Branch prediction
  Out-of-order execution
  Speculative prefetching
  Multithreading
  Multiprocessing
Further improvement:
  Domain-specific architectures

## Slide 4: Guidelines for DSAs
Use dedicated memories to minimise data movement
Invest resources into more arithmetic units or bigger memories
Use the easiest form of parallelism that matches the domain
Reduce data size and type to the simplest needed for the domain
Use a domain-specific programming language

## Slide 5: DNN Summary
Batches
  Reuse weights once fetched from memory across multiple inputs
  Increases operational intensity
Quantisation
  Use 8- or 16-bit fixed point or integer numbers
Operations
  Matrix-vector multiply
  Matrix-matrix multiply
  Stencil
  ReLU
  Sigmoid
  Hyperbolic tangent

## Slide 6: Matrix-Matrix multiplication

## Slide 7: Systolic array (2D pipeline)
Different from pipelining
  Nonlinear array structure, multi-direction data flow, each PE may have (small) local instruction and data memory
Different from SIMD
  each PE may do something different

## Slide 8: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 9: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 10: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 11: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 12: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 13: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 14: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 15: Computation example
Processing units arranged in a 2D grid
Each PU accumulates one element of the product

## Slide 16: Tensor Processing Unit
Google’s DNN ASIC
256 x 256 8-bit matrix multiply unit
Large software-managed scratchpad
Coprocessor on the PCIe bus

## Slide 17: TPU ISA
Read_Host_Memory
  Reads memory from the CPU memory into the unified buffer
Read_Weights
  Reads weights from the Weight Memory into the Weight FIFO as input to the Matrix Unit
MatrixMatrixMultiply/Convolve
  Perform a matrix-matrix multiply, a vector-matrix multiply, an element-wise matrix multiply, an element-wise vector multiply, or a convolution from the Unified Buffer into the accumulators
  takes a variable-sized B*256 input, multiplies it by a 256x256 constant input, and produces a B*256 output, taking B pipelined cycles to complete
Activate
  Computes activation function
Write_Host_Memory
  Writes data from unified buffer into host memory

## Slide 18: Tensor Processing Unit

## Slide 19: Tensor Processing Unit

## Slide 20: The TPU and the Guidelines
Use dedicated memories
  24 MiB dedicated buffer, 4 MiB accumulator buffers
Invest resources in arithmetic units and dedicated memories
  60% of the memory and 250X the arithmetic units of a server-class CPU
Use the easiest form of parallelism that matches the domain
  Exploits 2D SIMD parallelism
Reduce the data size and type needed for the domain
  Primarily uses 8-bit integers
Use a domain-specific programming language
  Uses TensorFlow

## Slide 21: FPGA vs ASIC

## Slide 22: FPGA vs ASIC

## Slide 23: Microsoft Catapult
Needed to be general purpose and power efficient
  Uses FPGA PCIe board with dedicated 20 Gbps network in 6 x 8 torus
  Each of the 48 servers in half the rack has a Catapult board
  Limited to 25 watts
  32 MiB Flash memory
  Two banks of DDR3-1600 (11 GB/s) and 8 GiB DRAM
  FPGA (unconfigured) has 3962 18-bit ALUs and 5 MiB of on-chip memory
  Programmed in Verilog RTL
  Shell is 23% of the FPGA

## Slide 24: Microsoft Catapult: CNN configuration

## Slide 25: Microsoft Catapult: Search Ranking Configuration
Feature extraction (1 FPGA)
  Extracts 4500 features for every document-query pair, e.g. frequency in which the query appears in the page
  Systolic array of FSMs
Free-form expressions (2 FPGAs)
  Calculates feature combinations
Machine-learned Scoring (1 FPGA for compression, 3 FPGAs calculate score)
  Uses results of previous two stages to calculate floating-point score

## Slide 26: FSM Example

## Slide 27: Microsoft Catapult and Guidelines
Use dedicated memories
  5 MiB dedicated memory
Invest resources in arithmetic units and dedicated memories
  3926 ALUs
Use the easiest form of parallelism that matches the domain
  2D SIMD for CNN, MISD parallelism for search scoring
Reduce the data size and type needed for the domain
  Uses mixture of 8-bit integers and 64-bit floating-point
Use a domain-specific programming language
  Uses Verilog RTL; Microsoft did not follow this guideline

## Slide 28: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero